## Slide 1
INDUSTRIAL COMPUTER VISION
Dent & Scratch Defect
Inspection — Back Glass
Current direction: interpretable, tunable Traditional CV
with Deep Learning / Hybrid as a controlled fallback.
CURRENTLY UNDER TEST
Controlled capture → local defect response → stable PASS / FAIL
INSPECTION SYSTEM
CAMERA
frame
LIGHTING
recipe
CV
decision
Defect families
Scratch = thin high-frequency structure
Dent = localized deformation / intensity anomaly
Core challenge
Reflective glass + micro-defects + video noise
→ glare / texture / dust can mimic defects
01

## Slide 2
01 • STATION ARCHITECTURE
Map the existing inspection station
Keep acquisition control modular; swap detectors without redesigning camera, lighting or capture control.
1
CAMERA
Basler Camera 1/2
Exposure • Gain • FPS
Resolution
2
LIGHTING
RGB recipes
Dual 4CH / Single 8CH
3
CAPTURE
Light ON → settle
Capture → Light OFF → save
4
DETECTION
RAW Laplacian • Canny
Pluggable detector registry
5
UI / RESULT
Live view + parameters
Detection result / PASS / FAIL
INTERFACE BOUNDARIES
Hardware boundary
Camera + lighting are controlled at acquisition stage.
Acquisition
Algorithm boundary
Detection is a pluggable module; Traditional CV and DL can share the same input protocol.
Detector
Decision boundary
Result is emitted as a stable inspection decision, not a raw pixel map.
UI / Result
02

## Slide 3
02 • CURRENT CV PIPELINE
Convert the inspection logic into one deterministic path
Each stage has a defined input, transformation, and rejection mechanism.
CONTROLLED
CAPTURE
Light ON
settle
capture
Light OFF
CLAHE
Local
contrast
enhancement
ROI /
BORDER
Canny / adaptive
threshold
+ erosion
LAPLACIAN
2nd derivative
→ |response|
LOCAL
THRESHOLD
μlocal + k·σlocal
SPATIAL
OUTLIER
centroid
neighbor count
TEMPORAL
PERSISTENCE
rolling mask
≥ hit rule
PARAMETER → PHYSICAL / ALGORITHMIC EFFECT
CLAHE grid / clip
local contrast scale
too local → texture amplification
Laplacian ksize
micro-detail scale
1/3/5/7 → detail vs robustness
k × σ
detection sensitivity
lower → more candidates + more noise
ROI erosion
border exclusion
protect structural edges
Neighborhood radius
physical search area
map to calibrated pixel / mm
Persistence frames / hits
temporal stability
reject transient flicker
DECISION OUTPUT
stable candidate map → PASS / FAIL; one-frame blips are rejected
03

## Slide 4
03 • DEVELOPMENT OPTIONS
Use a staged decision tree, not a leap to a new stack
Exhaust interpretable CV improvements first; benchmark learned approaches on the same controlled capture protocol.
PATH 1 • CURRENT
Traditional CV
Deterministic + tunable
Low data requirement
Fast iteration
Direct parameter ↔ physics mapping
Fallback trigger
Rule-based features cannot reach required robustness.
PATH 2 • FUTURE
Deep Learning
Controlled images
Phone / glass segmentation
Dent / Scratch / OK detection
Needs labeled data + validation
Model role
Learn complex appearance variation after the capture protocol is fixed.
PATH 3 • HYBRID
CV + Deep Learning
Raw RGB / grayscale
CLAHE + Laplacian
Local statistics + ROI masks
Spatial density + persistence
Model input
Engineered feature space + original appearance → learned decision.
COMPARE ON IDENTICAL PRODUCTION CRITERIA
Detection rate
False-positive rate
Minimum detectable defect
Processing time
Frame stability
04

## Slide 5
04 • VALIDATION & NEXT STEPS
Turn the prototype into a measurable inspection system
Validation must be tied to known defect size, location, capture repeatability, cycle time, and stable PASS / FAIL behavior.
A
DEFECT SET
Known dents + scratches
position / size metadata
B
OPTICAL REPEATABILITY
Multiple captures / part
lighting + exposure variation
C
CV TUNING
Sensitivity vs FP
pixel/mm calibration
D
DL BENCHMARK
Segmentation / detector
hold-out comparison
E
PRODUCTION TEST
Cycle time + stability
PASS / FAIL reliability
PRODUCTION KPIS
Detection rate
defects found
False-positive rate
nuisance candidates
Minimum detectable defect
size threshold
Processing time
per frame / part
Frame stability
temporal persistence
IMMEDIATE WORK PACKAGES
1
Optical setup
Fix camera pose, focus, exposure, RGB recipes
2
Ground truth
Build labeled library: type + size + location
3
Detector benchmark
Traditional CV → DL → Hybrid on same protocol
05